## Slide 1: John Lee Summer Project
Probability Based Surgical planning tool for balloon angioplasty

## Slide 2: Data Gathering

## Slide 3: Models
0080_0001 (Healthy)
0118_1000 (Alagille)
Healthy Models
  Artificially stenose models
  Helpful to know actual healthy values for uncertainty quantification later
Stenosis Models
  Have actual stenosis which must be identified
  Should have previously computed RCR boundary conditions
Notes: Model Issues
- Some models are not finely meshed/blended well and have issues constructing centerlines
- Ingrid’s models are in an older version of simvascular and must be reconstructed.

## Slide 4: Issues with Models
Some Models are not finely meshed enough to construct centerlines (Major issue, resolvable by reconstructing finer models)
  '0005_1001', '0119_0001', '0081_0001', '0084_0001’]
  SU0267, SU0269
We will move ahead with 1 model from Healthy (0080_0001), and 2 Models from Stenosis (0118_1000, SU0238)

## Slide 5: Healthy Models – BC tuning

## Slide 6: Healthy Models/ BC tuning
Yang et. al. 2019 Surrogate model (Modified)
Constant RCL values for MPA
C is computing assuming linear eh_r of 1.2e6 dynes/cm^2
MPA
Tunable RCR boundary conditions for LPA and RPA, with constant capillary wedge pressure of 7 mmHg
Objective Function (4 error terms summed)
Average Pulmonary Arterial Pressure (in mmHg)
  PiecewiseLoss( 12, 16, mPAP)
Max (systolic) Pulmonary Arterial Pressure (in mmHg)
  PiecewiseLoss( 18, 25, maxPAP)
Flow Split
  Squared Error Loss(.55 * mean_inflow, Q_RPA)
MSE vs flow
  Cubic spline of Q_RPA_flow (f(x) using interp1d)
  For n timesteps in inflow,
*PiecewiseLoss(lower, upper, sim)
  If sim > upper : ((sim – upper)/upper)^2
  If sim < lower: ((sim – lower)/lower)^2
  Else: 0
SquaredErrorLoss(target, sim)
  ((sim – target) / target) ^2
Split RCRS (Yang et. al. 2019)
RPA Tree and LPA Tree precomputed resistances
Optimization
Ideal: obj func < .001 (.1% error)
  Typically set lower and let it early stop.
Early stop: patience (5 iter), patience_tolerance (1e-6)

## Slide 7
Optimization Results/Sanity Checks (ex. 0080_0001)

## Slide 8: Issues w/
Lumped Multiple Objective optimization is slightly inaccurate (acceptable error)
Capacitance of MPA is computed using a default EH_R value (not a significant influence)
Resistance of RPA and LPA trees are a rough estimate from the automatic construction of the vessel tree
  We do not know if the RPA and LPA resistances appropriately correspond to the pressure drop across the tree.
  e.g. R_LPA = 5 cgs, R_RPA = 4 cgs -> ~.16 mPAP drop across the tree
Should the Capillary Wedge pressure of 7 be the target after the BCs or after the tree itself?

## Slide 9: Healthy Models - Artificial Stenosis

## Slide 10: Methodology
Construct a Branch Tree of the PA w/ generations
  Gen 0: MPA, Gen 1: RPA & LPA, …
Using the Branch tree, determine n possible branches to stenose in the first g generations
Use a y = poisson(𝜆 = 2*g) to determine how many locations exactly to stenose (this is subject to change)
Uniformly select y vessels from all n locations and give it an occlusion value from .75 - .9.
Make changes to R, C, L corresponding to occlusion change in the
Sample Stenosis only stenoses MPA (0), LPA (1,2,3), RPA (19).

## Slide 11: Healthy Models - Case Study 0080_0001

## Slide 12: 0D vs. 3D (Waveforms)
Base Solver
Method 1 (stenosis coeff)
M1 Solver
3D Solver
Notes:
mPAP drops to 1 in 3D solver?
3D solver uses different boundary conditions (does not consider rcr bcs)

## Slide 13: 0D vs. 3D (mPAP)
Base Solver
Method 1 (stenosis coeff)
3D
Not to scale
Notes:
Larger pressure drop across tree w/ M1. Similar to the pressure drop in 3D.
However, the 3D model seems a bit off/low. mPAP should be around 12 – 16, at least in inlet. May need to run own 3D

## Slide 14: 0D vs. 3D (maxPAP)
Base Solver
Method 1 (stenosis coeff)
3D
Not to scale
Notes:
Larger pressure drop across tree w/ M1. Less similar than mPAP, but still close.
3D model seems more reasonable here, with 23 mmHG down to 7.8.

## Slide 15: Waveforms
Base, No Changes
Proximal Stenosis (MPA, LPA, RPA)
Random Stenosis (Left) (includes LPA)
Notes:
Stenosis is rather extreme/common to obtain that pressure increase
Since Boundary conditions are tuned for healthy cases, they are not the most appropriate for the artificial stenosis
  We can see that the min PAP is dropping
  Do we need an Adaptive BC & how to do so
Rather odd that stenosing the Proximal vessels are not drastically increasing pressure.

## Slide 16
Proximal Stenosis
No Stenosis
Random Stenosis
Notes:
Hardly any pressure drop w/ None & Proximal
Significant Pressure Increase/Drop across tree with more stenosis Points.
Positive indication that stenosis is at least working, but must test with less occlusion @ less points
Not same scale
mPAP

## Slide 17
Proximal Stenosis
No Stenosis
Random Stenosis
Not same scale
max PAP
Notes:
Very similar to mPAP

## Slide 18: Next Steps w/ Healthy
Check with less stenosis and occlusion
Maybe consider a different way to select stenosis points
Double check realism?
  Run a 3D to compare
  Run 3D of stenosis case (to look at in the future)

## Slide 19: Stenosis Models – Stenosis Detection

## Slide 20: Stenosis Models
Only use models where an RCRT.dat file is provided for 3D simulations
  Must be mapped back to 0D style where face/cap names are also included in the file
Comes from both VMR & Ingrid’s previous models

## Slide 21: Identifying Stenosis Methodology
Construct a Branch Tree
Using
  a = 1.203e-4, b = 0.3927, c = 0.2381
  We assume order is roughly 16 – generation, since gen 0 = MPA = order 16
  https://journals.physiology.org/doi/full/10.1152/ajpheart.00123.2020
For a branch, compute the control resistance for that length. If the actual resistance is > r_threshold * control resistance, then we consider it a stenosis point. If not, we iterate through segments in the branch and repeat for the individual vessel segment
Alternative Proposal: Run a 0D simulation and observe the local effect where pressure drops > n%

## Slide 22: Stenosis Case Study Model - 0118_1000

## Slide 23: 0D vs. 3D (Waveforms)
Base Solver
M1 Solver
3D Solver
Notes:
M1 seems to capture 3D better in general, but still a little low
Waveforms seem kind of odd, do they need retuning?

## Slide 24: 0D vs. 3D (mPAP)
Base Solver
Method 1 (stenosis coeff)
3D
Notes:
Larger pressure drop across tree w/ M1. Definitely capturing flow/pressures drops better
0D Solver Bc’s were taken exactly from 3D simulation, so the 3D should be an exact match

## Slide 25: 0D vs. 3D (maxPAP)
Base Solver
Method 1 (stenosis coeff)
3D
Not to scale
Notes:
There is definitely a larger pressure drop w/ M1
3D model has a negative pressure at choke point in RPA? Is this even valid
  Ask in lab meeting

## Slide 26: Original vs. Fixed (Waveforms)
Fixed Solver
Notes:
Only Minor Reductions, as expected since most of the stenosis was encountered in the junction
Base Solver

## Slide 27
No Fix
Fixed Stenosis
Notes:
Minor decrease
mPAP

## Slide 28
No Fix
Fixed Stenosis
Notes:
Minor decreases too, particularly at ends
maxPAP

## Slide 29: M1 vs. Fixed (Waveforms)
M1 Fixed Solver
Notes:
There is a significant reduction in all parameters, indicating positive viability for this approach.
Also, there is actually no change in the vessels that were determined to be
***The fixing operation is slightly off, since it reduces the lumped stenosis coefficient in downstream branch vessels, only by the increase in the vessel’s radii, not considering the junction radii
M1 Solver

## Slide 30
No Fix M1
Fixed M1 Stenosis
Notes:
Clear decrease in pressure, but also a more even pressure drop between LPA and RPA
mPAP

## Slide 31
No Fix M1
M1 Fixed Stenosis
Notes:
Very large drop, with more even pressures.
maxPAP

## Slide 32: Stenosis Case Study Model – SU0238

## Slide 33: 0D vs. 3D (mPAP)
Base Solver
Method 1 (stenosis coeff)
3D
Notes:
Branch 93, Vessel 143, *Are some places with negative flow, but the pressure drop on average for that vessel is still positive (Is there an interpolation error???) The recorded outlet pressures are all around 20, which is not a huge drop?
Vessel by vessel, the min pressure out is around 17, (and the average pout is 19-20) which is to be expected. Hence I suggest some issue with interpolation.
Regardless, M1 is NOT capturing the 3D solution’s pressure drop.
Not to scale

## Slide 34: Other Potential Solutions

## Slide 35: Method 1 (being implemented)
Computing a stenosis coefficient only using input radii and output radii of a junction. Adding stenosis coefficient to downstream vessel.
Problems:
  May not be a good representation. Could drastically increase stenosis coefficient if input radii is really small. (Does not seem to be a huge problem as of right now)
  When performing stenosis fixture, it is not as easy to factor in stenosis coefficient reduction of vessel separately from the junction (doable though)
  May have errors mapping back into centerlines (possible issue)
  Does not work sufficiently with SU0238 (could be due to a different issue though)
Success
  Better representation with 0118_0001
  Only slightly elevating 0080_1000, which is good.

## Slide 36: Method 2
More intensive representation of branches, rather than just stenosis coefficient to downstream vessels
Problems
  May require much more involved changes to input file construction and mapping back to centerlines (not too familiar with code/no access)
  Perhaps already being planned to be implemented (Martin would know)
  Challenging to handle, since we can’t use Poiseuille laws easily

## Slide 37: Method 3 (Could go back and do later)
Given the nature of my task, we can run a 3D simulation “offline” first, then construct a more accurate representation of the 0D model using actual pressure drops across branches/segments
Could save at less number of timesteps to allow for faster computation of 3D solver, at cost of slightly less accurate optimization
Basically optimize the RCL for each branch such that an appropriate pressure drop/flow decrease is reached.
Problems:
  Very time intensive/code involved. May require more familiarity with vtk
  Concerns that 0D will not continue to match 3D if stenosis is introduced.
  How to segment the vasculature
Pros
  High likely to work/be accurate

## Slide 38: Suggestion for Next Steps
Tinker w/ Healthy models a bit more (We can guarantee that stenosis of healthy models will solely be in the vessels, hence not encountering the junction stenosis issue)
  Generate more models/case studies for healthy models.
  (~1 week, assuming no major issues)
Construct Neural network for 0D simulations on healthy models.
  (~1 week)
Compute Probabilities/Build tool
  (Back at ND)
*Uncertainty computation?
  (Back at ND)
*Go back and implement Method 3.

## Slide 39: Next Steps (Neural Network)
Construct NN capturing the changes in pressures and flows depending on the change in resistance
Sample from resistance space using Sobol Sampling
Compute Probabilities

## Slide 40
Pressures V143
Flows V143